# Inspection Tip Sheet

Wayne County / Jesup Ga.

# Reference Code For Construction From ICC

(International Code Council)

## Effective July 1,2007

- International Residential Code 2006 	 	        International Plumbing Code

- International Gas Code 2006			        International Mechanical Code 2006

- International Fire Prevention Code 2006                       International Building Code 2006

- International Energy Conservation Code 2006              National Electric Code 2008

* Code may also include Ga. amendments  and local jurisdiction  additions

- Ga amendments  web site  www.dca.state.ga.us

- Building code web site  www.iccsafe.org

Inspections  before a

Inspections                                         Reinspection fee is charged

1. Footing	1

2.Temporary Power	1

3.Open  Plumbing	1

4.Cover-up	2

5.Permanent Power	1

6.Final/C.O.	2

Occupancy with-out  a C O is prohibited !!!

All inspection require 24 hour notice.

Tip sheet are not intended to be inclusive. It is the responsibility of the contractor to build to  minimum Ga codes.

Contractors are required to be licensed. Contractor and subs. will have business license somewhere in Georgia.

Oversight on Wayne County Building Inspection Department,does not negate the contractors responsible to build to minimum codes.

Inspection:  Footing

General

- Permit must be posted  in job box before calling in ( to remain on site until c.o. is issued)

- Port-o-let

- Check set back – property corner marked

- Trash receptacle on site/or approved method

- All culverts must be concrete / Driveway 24’ wide

Footing

- Footing depths into natural soil( 12” )

- Grass ,roots and wood removed from house foundation area

- Grade stakes/w chairs to tie   rebar

- One and two  story 10” x 20” with 2 # 5 rebar

- Minimum Lap 25”

- Up to 3’wall,  1 vertical # 5 rebar on 8’ centers

- Over 3’ wall, 1 vertical #3  rebar on 4’ center

- All  cells  must be filled./grouted

- All verticals  must be hooked with 90 turn on bottom  (303A)

- Wood floors  will have Bond beam with 1 # 5 rebar continuous   (303B)

- No 4” partition blocks on garage.

# Inspection:  Temporary Power

- Respective power company minimum standards/NEC

- Minimun one GFCI  with weather-proof cover

- Secure to post ,wire connection tight, boxes clean w/no extra knock-outs open

- Interior covers must be in place

# Inspection:  Open Plumbing tips

1. All waste and water lines expose for inspection

2. Water line pressure 100 psi.

3. Waste line pressure( 10’ head pressure of water or 5 psi  air)

4. Sleeving of wastelines  thur foundation walls with larger Diameter pipe

5. Insulation of pipes for protection of breakage or corrosion.

6.Minimum water service ¾”, three bathrooms 1” Service	.

7.Accessible shut off for house.

# Inspection:   Pre-Slab/Sub Floor Tips

### Pre-slab

1.  Minimum thickness of slab 3 ½”

2.  Vapor Barrier under any area of habitable space or possible space in the future (porches,garage)

3.   Termite  Treatment

4…Elevation certificate if in a flood zone

- 5/8” anchor bolts 10” long , minimun 7” in concrete, 20” on center around house with          3”x 3”washers , 1/8” thick

- Approved mud sills  accepted.

- Above 5 Blocks require compaction test.

### Subfloor

1.  Elevation certificate if in a flood zone

2.  Anchoring in foundation walls/piers, same as slab, figure 303 b

3...Access opening in foundation wall 18” x 24” no equipment/22” x 30” w/ equipment(clear)

4…Ventilation to meet  minimum code( within 3’ of all corners, on  opposing walls,1 sq ft for every 150 sq ft,1 sq ft for every 1500 sq ft with moisture barrier )

5…Beams, girders, and joist in place

6.   Grading under sub-floor to be at or near outside grade

# Inspection: Cover-up / Dry-in Tips

- Base plates anchored to slab with in 6 to 12 inches of each end of plate and corners

- Stud notching  and boring;  non bearing wall, boring 60% or 40% notching; load bearing wall, 40%  boring or 25% notching.60% boring if double studs, no more 2 successive studs; holes no closer than 5/8” to face.

- Corners exterior-3 studs minimum with  top plates overlapping at corners and bearing walls.

- Re-enforcement straps on top plates over 50 % of plate  notched or bored (16 ga with 8-16d nails each side).

- Joist  boring or notching, nothing in the middle 1/3 span, holes minimum 2” from top or bottom in the outer 1/3 span. Notching maximum 1/6 depth or notch at the end for ledger ¼  maximum depth ( conventional lumber ).

- Check manufacture’s guide lines on drilling/notching of laminated beams and tji’s.

- Stud sizing & spacing:  2x4 up to 10’ in height 1 story supporting roof & ceiling 24” o.c. (utility grade 16” oc).   2x4 supporting roof & ceiling plus 1 floor 16”oc or 2x6 24” oc roof & ceiling & 2 floors 2x6 16”oc.

- Check spans on joists, rafters, beams, and headers in relation to sizing. All sheathing minimun 7/16”osb , nailed 6”on center for edge spacing, 12” in the field, sheathing must attach to bottom plate and top member of db. top plate.  8d nails. Horizontal joints shall occur over framing.

- Where windows and doors interrupt sheathing, framing anchors shall be used. Figure 305d

- Gable end-walls and two stories sheathing shall not break at ceiling or floor  levels, lap over

- Roof sheathing shall nail 6”on center ,6” in field, 4” on end gable or gable truss. 8d nail

- Shingles will have minimun of 6 fasteners per shingle. Metal roof per manufacture installation for 100 mph.

- Stairway treads, risers and head clearance.  Tread minimum 9”, raiser height 7 ¾” maximum and 6’8” minumum head clearance measured vertical from nose to tread.

- Minimum stairs width 36”.

- Minimum tread on winder stair 6” at narrowest point and 10” at 12” from inside point.

- Landing minimum 36” x 36”.

- Rafter sizing/spacing and knee wall supports to break spans.

- Knee wall support spacing maximum 48” with plate and purlin.

- Attic access opening to be minimum 20” x 30” or large enough to remove appliances or be accessible by pull down stairs or other permanent steps.

- Attic access openings double framing if perpendicular to joists.

- ½” sheetrock on garage walls common to house,5/8” type X on ceiling if room above

- Pull down stairs in garage need minimum 3/8” fire retardant structural panel to meet fire separation.

- Multi dwelling unit separation.

- Attic decking to equipment (minimum 24” wide, maximum travel distance to equipment 20’).

- Minimum work area for equipment 30” x 30”(  H & A or water heaters).

- Raising decking to allow for r-30 insulation.

- Joist notching for ledgers maximum 25% depth of member.

- Ledgers minimum size 1.5” actual.

- Ledger nailing on each side of supported member.

- Maintain sleeping room egress (5 sq ft ground floor, 5.7 sq ft 2nd floor and above) also with minimum width 20” and height 24” and sill height above floor 44” maximum.

- Habitable minimum rooms sizing as per code (1 room 120 sq ft, kitchen 50 sq ft, other room 70 sq ft).

- Glass tempering (over tub, in stairways, within 24” of door arc while closed, less than 18” above finish floor and greater than 9 sq ft in single pane).

- Windows installed and flashed  per manufacture instruction.

#### Mechanical

1.  Units set with drains for condensation and pan.

2.  All ducts installed and sealed (supply & returns).

3.  Flex duct bends (maintain correct bend radius).

4.  Duct line support spacing (metal maximum 10’, flex manufacturer instruction).

5.  2” clearance between chimney flue and combustible materials.

- 20’ maximum travel distance to equipment in attic or under floor areas.

- Vents on exhaust fans

- Pipe protection –1 ½” from edge of member, 2” below top plate/above sole

- Fuel gas protection-1 ½” edge of member, 4” below top plate/above sole

Plumbing

- Reinforcement strapping for framing violations to studs and top plates.

- Boring & notching of joist (floor or ceilings).

- Water hammers on all fixtures with quick closing valves (toilets, washing machines, dish washers, ice makers, etc…).

- Pressure on water lines .

- Top out pressure on waste lines if there is a 2nd floor bath or ½  bath.

- At least 1 vent pipe to exterior minimum 1 ½” (but calculate reference fixtures) and located as specified by code.

- Water heater relief line and pan drain line.

- Waste line supports maximum spacing 48”.

- All plumbing lines protected from nails less 1 ½”from edge.2”below top plate/above sole

- Air admittance valves ok under sinks 4” above drain, always accessible minimum 6” above insulation in attic.

- Waste line cleanouts; 1 for 40ft with more than one change of direction, any change of direction over 45 degrees, under floor cleanout not more than 20’ from access door.

- Minimum 15” clearance- finished side wall to center of  toilets-

- Gas lines will need to be pressured to minimum 10 psi.

- Gas lines protection –minimum 1 ½”  from edge 4” below top plate/above sole/to each side

- Maximum 20’ travel distance to water heaters in attic.

- minimum 2 hose bibbs

##### Electrical

- Lights in required locations.

- Receptacles in required locations,

- light and receptacle in attic for appliance, recpt, near outdoor appliance.

- Smoke detectors in required locations (bedrooms , outside bedrooms and at each level).

- Two separate circuits to kitchen area minimum 20 amp.

- Whirlpool tub motor GFIC in accessible location

- Wiring protected  within 6’ of attic access.

- Panel location and work space (not allowed in bathrooms, toilet rooms or clothes closets).

- Arc-fault  protection  as stated Secton 210.12

- Wire protection from nails if less than 1 ¼” from edge

- secure within 12” of box

12. Carbon Monoxide  detectors in vicinity of bedrooms (Jan 2009)

13.All areas specified in 210.52, all 125 volt,15 and 20 amp recpt. Shall be tamper-resistant

Inspection  :  Permanent Power Tips

##### Permanent Power

- Panel completely made up (interior and exterior).

- Fixtures installed or wire nuts or taped.

- Disconnects at required locations.

- Arc fault and GFIC  breakers for required locations.

- Bonding bar removed from panel box where required.

- Proper grounding in relation to power company.

- Resistance to ground  25 ohms

Inspection:  Certificate of Occupancy Tips

##### Mechanical

- Breaker sizing to unit requirements.

- Condensation and pan drain lines and turn downs.

- Equipment disconnects.

- Exterior equipment minimum 2” above finished grade.

- Clean foreign objects from overflow plan.

##### Electrical

- Panel box labeling.

- All fixtures installed.

- Breaker sizing to appliance requirements.

- GFIC breaker and receptacle functioning properly and to proper locations.

- Arc fault breaker functioning properly and to proper locations.

- Smoke detectors functioning properly.

- Verify disconnect.

- Verify equipment above base flood elevation if in flood hazard location.

##### Plumbing

- All fixtures installed.

- Turn downs on relief lines and drain lines.

- Insulation of water lines in non-insulated space.

- Waste line support spacing (sub-floor).

- Water heater operational and correct at fixtures.

- Drain pan if water heater in attic w/ drain line

- Accessible service cut off (gate valve after meter).

- Accessible shutoff each fixture exc tub & shower

- Exterior pipe penetration must be chaulked

##### Building

- Seal around exterior wall violations.

- Handrails & guardrails on stairs, balconies, porches & steps (handrails required if stairs/steps are over 30” high with handrail at minimum height 34” and maximum height 38” ; guardrails on balconies and porches raised over 30” high requires rail minimum 36” high with less than 4” opening between pickets).

- Weather stripping around doors and attic access(interior).

- Exterior door locks single cylinder (no key inside).

- Whirlpool motor access.

- Grading around home (6” fall away within 10’).

- Weep holes in brick veneer 33” oc.

- Separation of habitable space from garage and attic (minimum ½” sheetrock).fire rated pull-down if in garage. Carports not open on at least two sides will be considered a garage.

- Hearth extensions on fire places (16” front, 8” side on less than 6 sq ft, 20” front, 12” side if over 6 sq ft).

- Exterior wood siding or trim minimum 6” from finished ground.

- Building Address numbers legible from the street.

###### Insulation  Zone 2

Residential  energy efficiency

- Ceilings- R-30   Cathedral  R-19

- Walls   R-13

- Floors R-13

- Kneewalls R-18 with sheathing on attic side