BID NOTICE

Sealed bids will be received for “Gardi-Broadhurst Road Drainage Improvements” in the Wayne County Administrator’s office, 341 East Walnut Street, Jesup, Georgia 31546 until 10:00 A.M., Tuesday, October 18, 2016, at which time they will be publicly opened and read.  A contract will be awarded at a regular scheduled meeting of the Board of Commissioners in the County Administrator’s Office, 341 East Walnut Street, Jesup, Georgia 31546.

The work under this contract will consist of the following:

Furnish all material, labor, tools, equipment, supervision and incidentals to replace 144 lineal feet of 24” diameter and 140 lineal feet of 48” diameter reinforced concrete pipe cross drains including all traffic control, E&SC BMP’s, excavation, backfill, and pavement repairs.  In addition, after completion of pipe replacement, place approximately 1500 tons of asphaltic concrete leveling and surface courses as project budget allows.

All work shall be done in accordance with the latest revision of Georgia Department of Transportation’s Standard Specifications.  Contractor must be approved as a GADOT contractor.

All questions concerning the work should be addressed to Bill Shuman, County Engineer at 341 East Walnut Street, Jesup, Georgia 31546, telephone 912-427-5900 (office) or 912-258-5162 (cell) or Elton Aspinwall, County Road Engineer telephone 912-202-4064 (cell).

Bids must be accompanied by a certified check or Bid Bond in the amount of five percent of the amount bid.  The successful bidder must be able to provide a Payment Bond and Performance Bond for the total (100%) contract amount.  A statement from the bidder’s bonding company shall accompany the bid bond stating that the bidder can submit a Payment and Performance Bond, in accordance with the contract documents, within ten days of award of contract.  The low bidder must furnish proof that they are a Georgia Department of Transportation Certified Contractor before a contract will be executed.

The Wayne County Board of Commissioners reserves the right to reject any or all bids and to waive technicalities and informalities. The Owner reserves the right to award the Contract in the best interest of the Owner.

Wayne County Board of Commissioners

County Administrator

341 East Walnut Street

Jesup, Georgia  31546